## Slide 1: Motion Planning for Multiple Autonomous Vehicles
Rahul Kala
Reaching Destination before Deadline with Intelligent Transportation Systems
Presentation of the paper: R. Kala, K. Warwick (2014) Computing Journey Start Times with Recurrent Traffic Conditions, IET Intelligent Transport Systems, DOI: 10.1049/iet-its.2013.0082

## Slide 2: Key Contributions
Decentralized agents at the intersections are proposed which record the traffic speeds and variations along with time. The use of centralized agents (or single agent systems) for such an approach is common, which is however not a scalable approach. The use of decentralized agents for traffic speeds is also common. Here recording an extra deviation factor helps in answering the user query.
A new problem of start time prediction is studied, where a user may adapt the algorithm based on the penalty of late arrival. A single factor governs the performance. Guidelines enable a user to set the parameter.
Using the existent notion of advanced driver information system, the twin problems of start time prediction and routing are solved.
A graph search method is proposed to compute the route and the start time for the vehicle. The algorithm attempts to select a route which is the shortest in length, has a high reliability and gives the latest starting time.

## Slide 3: Assumption
All roads can get very congested
There may be no alternative roads
Recurrent traffic (historic traffic trends are repeated)
No communication
Concept
Distribute traffic in different times of the day

## Slide 4: Problem
Learn Historic Traffic Trends
Calculate Start Time so as to reach destination at pre-specified time
Calculate Route so as to reach destination at pre-specified time

## Slide 5: Problem
Important
Somewhat important
Not at all important
E.g. Watching a movie
Going for a leisure trip
E.g. Meeting friends
Very Important
E.g. Catching a flight
How important is reaching on time?
Importance of reaching on time

## Slide 6: Problem
Knowing traffic trend at the intended time of travel
Knowing changes in traffic trends
Enough experience with all alternative routes/ times to know uncertainties
Enough experience to tune start time/ route to perfection
Knowing the various possible routes
Considerations for human drivers to enable selection of the best route and start time
If these are true (e.g. going to office) human judgement is better, if not machine judgement is better

## Slide 7: Problem
Assuming average travel speeds is sub-optimal
It doesn’t capture
  Changing trends at different times of the day
  Generally increasing/ decreasing density of traffic along with time
  Uncertainty associated with the captured speed, and hence the travel
  Don’t tradeoff between maximizing start time and probability of reaching on time

## Slide 8: Problem
For every intersection
For every type of day
For every time
Learn Average Speed
Learn Speed Variation
Learnt Information
Place intelligent agents at every intersection
Monitor all vehicles
Update learnt metrics
Learning Part
Use graph search for the road network graph
For every road in search
Use learnt metrics for cost computation
Query Part

## Slide 9: Objectives
Start as late as possible
Select fastest route
Probability of reaching on time should be highest
In case of early arrival, wait time should be least

## Slide 10: Learning Stage
Road Network Graph
Intelligent Agents Placed at every intersection
Road
Monitor all incoming vehicles
Learn
average speed and variation

## Slide 11: Learning Travel Speeds
Learning Primitives
Traffic on similar days would be similar
  E.g. Traffic throughout the day on Wednesdays and Thursdays would be similar
Traffic would be similar in intervals of 10 minutes
  Too small interval = too many parameters to learn, which may hence be difficult and uncertain.
  Too large interval = high deviation of speeds within the time interval.

## Slide 12: Learning Travel Speeds
  New average speed = lr*new observed speed + (1-lr)*old average speed.
  lr = learning rate
Store all recent speeds to compute variations
Small lr = algorithm behaves passive and does not capture any changing trend
High lr = algorithm may treat any delay due to immediate uncertainties as a change in trend

## Slide 13: Learning Travel Speeds
Centralized Architecture (one agent stores and processes all information)
Decentralized Architecture (an agent at every intersection)
One connection per vehicle
Too many queries in total by all the vehicles
Multiple connections to all intersections of competitive routes
Computation spread across agents and hence manageable

## Slide 14: Learning Travel Speeds
Dealing with immediate non-recurrent traffic
Observed speed too different from current average, immediate non-recurrent traffic, pause learning
If same continues in the future, new trend, continue learning
If non-recurrent traffic is due to pre-known events, manually pause learning

## Slide 15: Routing
Fuse the different objectives in a single cost function
Use a standard graph search on the road network graph
Return the corresponding route and start time
Working methodology

## Slide 16: Routing
Cost function:
Latest time to reach a node so as to expect to reach the goal at the pre-specified time

## Slide 17: Routing
S. No. | Property | Normal Graph Search | Used Graph Search
1. | Cost Function | Distance from source (say) | Latest time to leave to reach goal
2. | Source/ Goal | Cost for source is known (0) while goal is to be found | Cost for goal is known (set reaching time) while source is to be found (start time)
3. | Direction | From source expand till reaching goal | From goal expand till reaching source
4. | Output | Minimum distance from source to goal (cost), route from source | Minimum time from source to goal (cost), route from source, start time
The search is inverted (due to S. No. (2))

## Slide 18: Routing
Finding latest time to leave a general node (or source)
is same as maximizing start time (for source)
is same as minimizing delay in case of an early arrival
is same as minimizing travel time
is opposite to maximizing probability of reaching on time (the earlier, the better)

## Slide 19: Routing
Travel speeds are stochastic
Stochastic graph search is computationally expensive
A deterministic cost function maintaining tradeoff between the contrary objectives is to be found
Or, a specific speed is to be chosen for every road, based on the observed data

## Slide 20: Routing
Number of vehicles
Observed Speeds
Observed speeds of each vehicle
learning data
Assumed distribution the from learnt data
Choose a speed to compute the cost function, for every road

## Slide 21: Routing
Number of vehicles
Observed Speeds
Choose a speed to compute the cost function, for every road
Too optimistic – assuming speed to be one of the highest speeds in the historic data
Too pessimistic– assuming speed to be one of the lowest speeds in the historic data
Pessimistic
Optimistic
Average

## Slide 22: Routing
Number of vehicles
Observed Speeds
Choose a speed to compute the cost function, for every road
Average Speed
Risk region = α.Deviation
Deviation
Speed assumed for cost computation

## Slide 23: Routing
Chosen speed = Average Speed - α.Deviation
α is a user chosen parameter as per task (maintains tradeoff between contradictory objectives)
More importance of reaching on time = more resistance to risk = higher α, and vice versa
High α = more resistance to risk = earlier start time = high probability of reaching, and vice versa
High deviation = vehicles in that road vary largely in speed = road is less reliable and should be avoided = larger resistance to risk, and vice versa

## Slide 24: Routing
If the data for a specific road (for a specific similar day/time) is too less, learnt speed is unreliable, despite deviation.
High reported deviation = reported unreliable road (desirable)
Low reported deviation = reported reliable road (undesirable)
Hence minimum deviation is fixed

## Slide 25: Probability of reaching on time
Converting α into a probability to enable use setting α
Simulate the system for various α for a region
For each simulation compute the percentage of vehicles reaching late
Draw a graph between α and the other metrics
User can read this graph and decide the value of α

## Slide 26: Results
Chart: Deviation from time to reach goal
| 100 | 75 | 50 | 25 | 0 | -25 | -50 | -75 | -100 | -125 | -150 | -175 | -200 | -225 | -250 | -275 | -300 | -325 | -350
α=0 | 0 | 0 | 0.5 | 4 | 19.5 | 47 | 26 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
α=0.25 | 0 | 0 | 0 | 0.5 | 8 | 13.5 | 42 | 32 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
α=0.5 | 0 | 0 | 0 | 0 | 0.5 | 5 | 18 | 39.5 | 29.5 | 7 | 0.5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
α=0.75 | 0 | 0 | 0 | 0 | 0 | 2 | 2.5 | 17.5 | 26.5 | 37 | 11 | 3.5 | 0 | 0 | 0 | 0 | 0 | 0 | 0
α=1 | 0 | 0 | 0 | 0 | 0 | 0 | 0.5 | 1 | 9 | 19.5 | 30 | 23.5 | 13 | 2.5 | 1 | 0 | 0 | 0 | 0
α=1.25 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.5 | 3 | 13 | 20.5 | 30.5 | 17.5 | 9.5 | 4 | 1.5 | 0 | 0
Ideal reaching time
As α increases, vehicles get less late, and reach more earlier

## Slide 27: Results
Chart: Deviation from time to reach goal
| 100 | 75 | 50 | 25 | 0 | -25 | -50 | -75 | -100 | -125 | -150 | -175 | -200 | -225 | -250 | -275 | -300 | -325 | -350
α=0.125 | 0 | 0.5 | 0 | 1.5 | 9 | 30 | 39.5 | 19.5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
α=0.375 | 0 | 0 | 0 | 1.5 | 2.5 | 11 | 29.5 | 42 | 11.5 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
α=0.625 | 0 | 0 | 0 | 0.5 | 0 | 1 | 8.5 | 32 | 36 | 20 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
α=0.875 | 0 | 0 | 0 | 0 | 0 | 0 | 0.5 | 4.5 | 24 | 35.5 | 21.5 | 12 | 2 | 0 | 0 | 0 | 0 | 0 | 0
α=1.125 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.5 | 2 | 11.5 | 26.5 | 25.5 | 18 | 7.5 | 6 | 2 | 0 | 0.5 | 0
Ideal reaching time
As α increases, vehicles get less late, and reach more earlier

## Slide 28: Results
Chart: α
| 0 | 0.125 | 0.25 | 0.37500000000000056 | 0.5 | 0.62500000000000122 | 0.75000000000000122 | 0.87500000000000122 | 1 | 1.125 | 1.25
Without cooperation | 23 | 11 | 8.5 | 4 | 0.5 | 0.5 | 0 | 0 | 0 | 0 | 0

## Slide 29: Results
Chart: α
| 0 | 0.125 | 0.25 | 0.37500000000000056 | 0.5 | 0.62500000000000122 | 0.75000000000000122 | 0.87500000000000122 | 1 | 1.125 | 1.25
Without cooperation | 3.66 | 1.97 | 1.25 | 0.685 | 0.06 | 0.13 | 0 | 0 | 0 | 0 | 0

## Slide 30: Thank You
Acknowledgements:
Commonwealth Scholarship Commission in the United Kingdom
British Council