## Slide 1: Motion Planning for Multiple Autonomous Vehicles
Rahul Kala
Multi-Level Planning
Presentation of the paper: R. Kala, K. Warwick (2013) Multi-Level Planning for Semi-Autonomous Vehicles in Traffic Scenarios based on Separation Maximization, Journal of Intelligent and Robotic Systems, 72(3-4): 559-590.

## Slide 2: Why Graph Search?
Completeness
Optimality
Issues
Computational Complexity
Key Idea
Hierarchies

## Slide 3: Key Contributions
To propose a general planning hierarchy in an assumed complex modelling scenario, where any algorithm may be used at any level of hierarchy.
To use simple heuristics such as separation maximization, vehicle following and overtaking, to plan the trajectories of multiple vehicles in real time.
An emphasis is placed on the width of feasible roads as an important factor in the decision making process.
The developed coordination strategy is largely cooperative, at the same time ensuring near-completeness of the resultant approach and being near-optimal for most practical scenarios.

## Slide 4: Key Definitions
Term | Definition
Pathway | Closed region of roads such that no obstacle lies inside it. Decides manner of avoiding the obstacles.
Pathway Segment | Fixed length segments along the length of the road constituting a pathway.
Distributed Pathway | Strategy of distributing a pathway segment amongst the individual vehicles projected to lie at the same time

## Slide 5: Algorithm
Road Selection
Pathway Selection
Pathway Distribution
Trajectory Generation
Vehicle to be planned
Road/Crossing Map
Path
Pathway
Distributed Pathway
Trajectory
Replan
All Vehicle Pathways
All Vehicle Trajectories
Controller
Replan

## Slide 6: Hierarchies*
Pathway Selection
Obstacle Avoidance Strategy
Select widest and shortest length pathways
Pathway Distribution
Arrange vehicles projected to lie in a pathway segment
Prioritization to decide vehicle relative order
Trajectory Generation
Spline curves
Feasibility check
Separation maximization to decide vehicle position
Local optimization
* This presentation was intended to supplement the thesis. The paper lists an additional hierarchy of route selection as hierarchy 1, and henceforth all hierarchies get incremented by 1

## Slide 7: Coordination basics
Layer-by-Layer
Each level shares its result with same level of the other vehicle
A vehicle can ask any other to re-plan at any level depending upon priorities

## Slide 8: Hierarchy 1: Pathway Selection
Traverse a sweeping line across the road length in small steps
Find areas (Pathway Segments) without obstacles in this line
Connect the obstacle free areas to produce a graph
Search this graph for widest and smallest path (Pathway) to the end of the road
Assuming a single vehicle only
Related terminology | 
Pathway segment end centre | Centre of the sweeping line in the obstacle free region
Pathway segment | Area bounded by the consecutive line sweeps in the same obstacle free region

## Slide 9: Separation Maximization
Separation
Pathways
Vehicle Placement

## Slide 10: Hierarchy 1: Pathway Selection
Sweeping line to compute pathway segments
Pathway Segment
Pathway Segment End Centre
Dijkstra’s Output
Current Position
Optimal Pathway
Line denoting connectivity of two pathway segments

## Slide 11: Hierarchy 1: Pathway Selection
For multiple vehicles
Traverse a sweeping line across the road length in small steps
Find areas (Pathway Segments) without obstacles in this line
Connect the obstacle free areas to produce a graph
Search this graph for widest and smallest path (Pathway) to the end of the road
For every edge/pathway segment
Extrapolate the motion of the other vehicles by their pathways
List vehicles using the same pathway segment at the same time
Classify the vehicles into higher priority and lower priority
For every higher priority vehicle, subtract wmax from the segment width
Replan lower priority vehicles at the pathway level
Replan lower priority vehicles at the distributed pathway level
To make the other vehicles account for this plan

## Slide 12: Hierarchy 1 Prioritization
Ri is said to have a higher priority over Rr if
Ri and Rr are driving in the same direction and Ri lies ahead of Rr, or
Ri and Rr are driving in opposite directions point of collision lies on the left side of the complete road (because Rr is in the wrong side)

## Slide 13: Hierarchy 1 Speed Adjustments
If unable to generate a feasible pathway: find the higher priority vehicle ahead blocking the road segment and follow it (reduce speed)
Else select a new route –blockage avoidance

## Slide 14: Hierarchy 2: Pathway Distribution
Need to plan a bunch of affected vehicles
Vehicles planned in a prioritized manner, vehicle ahead gets more priority

## Slide 15: Hierarchy 2: Pathway Distribution
For every pathway segment in pathway
Extrapolate and list vehicles using the same pathway segment at the same time
Classify the vehicles into higher priority and lower priority
Keep relative placing: higher priority, vehicle under planning, lower priority
Divide segment width equally amongst vehicles and hence compute position
Pathway segment
Obstacle or road boundary
All higher priority vehicles line here
All lower priority vehicles line here
Vehicle being
planned lines here
Attempt to tune infeasible paths for feasibility
If still infeasible, re-plan lower priority vehicle at pathway selection level
If still infeasible, reduce speed and follow

## Slide 16: Separation Maximization
Vehicle Placements
Pathways

## Slide 17: Hierarchy 2 Prioritization
Design of priority scheme such that higher priority vehicles are relatively on left and lower ones of the right
Ri has a higher priority if
it lies ahead of Rr with Ri and Rr going in the same direction, or
Rr and Ri are travelling in different directions
Implementation of behaviours of overtaking on the right, being overtaken on the right and drive left

## Slide 18: Pre-preparation and Post-preparation
Pre-preparation: Rather than going very near to a vehicle and then aligning to avoid it, take relative position well in advance
Post-preparation: Rather than quickly returning to the centre after having avoided a vehicle, stay at the same relative position for some time
Both strategies followed in case no other vehicle is present

## Slide 19: Pre-preparation and Post-preparation
Pre-preparation
Post-preparation
Too close
Too close

## Slide 20: Hierarchy 2: Pathway Distribution
Vehicle 1
(Speed=5)
Vehicle 2
(Speed=5)
Vehicle 3
(Speed=15)
Overtake
Pre-preparation

## Slide 21: Hierarchy 3: Trajectory Generation
Trajectory smoothening
Spline curves
Collision
  For vehicles in the same side: Lower priority vehicle replans, else vehicle follows the lower priority vehicle ahead
  For vehicles in the opposite side: Decrease speed iteratively and re-plan
Local optimization for greater smoothness

## Slide 22: Hierarchy 3: Trajectory Generation

## Slide 23: Hierarchy 3: Trajectory Generation
Vehicle 2
(Speed=5)
Vehicle 1
(Speed=5)
Vehicle 3
(Speed=15)

## Slide 24: Results

## Slide 25: Results – Single Vehicle

## Slide 26: Results – Two Vehicles

## Slide 27: Results – Two Vehicles

## Slide 28: Results - Multi Vehicle

## Slide 29: Results - Overtaking

## Slide 30: Results – Vehicle Following

## Slide 31: Analysis
Path length v/s ρ
Time required for optimization v/s ρ.
Speed of traversal of vehicle v/s ρ

## Slide 32: Analysis
Time of travel of vehicle v/s ρ
Time of optimization v/s Δ

## Slide 33: Analysis
Chart: Number of Obstacles
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
 | 0.46129 | 0.46644 | 0.4955 | 0.51634 | 0.54925 | 0.59359 | 0.5623 | 0.60155 | 0.6284 | 0.62641 | 0.64677
Chart: Number of Vehicles
 | 0.45746 | 0.6767 | 0.4991 | 1.0804 | 2.4904 | 3.5093

## Slide 34: Thank You
Acknowledgements:
Commonwealth Scholarship Commission in the United Kingdom
British Council