## Slide 1: Motion Planning for Multiple Autonomous Vehicles
Rahul Kala
Dynamic Distributed Lanes
Presentation of the paper: R. Kala, K. Warwick (2014) Dynamic Distributed Lanes: Motion Planning for Multiple Autonomous Vehicles, Applied Intelligence, DOI: 10.1007/s10489-014-0517-1

## Slide 2: Why Graph Search?
Completeness
Optimality
Issues
Computational Complexity
Key Idea
State Reduction: Select which states to expand

## Slide 3: Key Contributions
The generalized notion of lanes is defined.
The generalized notion is used for planning and coordination of multiple vehicles.
A pseudo centralized coordination technique is designed which uses the concepts of decentralized coordination for iteratively planning different vehicles but empowers a vehicle to move around the other vehicles. The coordination is hence better in terms of optimality and completeness than most approaches (discussed so far) while being somewhat computationally expensive in the worst cases.
The concept of one vehicle waiting for another vehicle coming from the other direction is introduced, when there may be space enough for only one vehicle to pass.
Heuristics are used for pruning the expansions of states, which result in a significant computational efficiency while leading to a slight loss of optimality.

## Slide 4: Defining (Virtual) Lanes
Properties | 
Distributed | The number of lanes and their widths may change in different segments of the road
Dynamic | The lanes change along with time for every pathway as the vehicles pass by.
Single Vehicle | No two vehicles may occupy a lane side-by-side
Variable Width | Every lane has a different width

## Slide 5: Solution Approach
A general graph (here Uniform Cost Search) search can be used with:
  High resolution maps
  Rich action set for the vehicle
To solve within computational time, the number of states expanded needs to be restricted
Coordination strategy needs to be devised

## Slide 6: State Reduction
Reduction hypothesis:
Vehicles maximize lateral separations
Vehicles prefer to travel at same lateral positions along the road

## Slide 7: State Expansion
Consider expansion of a state L
Problem is selecting child states L formed as a result of the expansion
Only expansion step of the graph search algorithm is discussed in this work, while the rest of the algorithm is same as a general graph search.

## Slide 8: Considering only a Single Vehicle

## Slide 9: State Reduction
Use a sweeping line (Z) for obstacle analysis in large steps
Select regions of line (Pathways) in obstacle free regions
Select best point inside every pathway (L3)
Make these children and connect to parent (L) by a smooth trajectory
Select similar point (L2) at an earlier sweeping line (Z2)
Feasibility analysis
Vehicle Placement Hypotheses
(i) Maximize lateral separations
(ii) Attempt to drive in same relative position at the road

## Slide 10: State Reduction
Sweeping line used for obstacle analysis (Z)
L
All pathways
(3 expansions to be done)
A pathway
Vehicle position at extremity of pathway
Y’
Earlier sweeping line for expanded node (Z2)

## Slide 11: Why use L2 and not L3?
Or why select a state not at the sweeping line but earlier?
Or why Z2 and not Z?
Sweeping Line
Best point L3
Obstacle
But if vehicle lands at L3, it cannot steer sharp enough and avoid the obstacle
Z
L

## Slide 12: Why L2 and not L3?
Vehicle expected to align itself at L2 for obstacle seen at L3
If vehicle can go from L to L3 via L2, it is safe at L2
Curve from L to L2 may be traversed if optimal
Curve from L2 to L3 is only for connectivity check/obstacle analysis
L3 acts as a roadmap for L2 informing it about any obstacle well in advance before the vehicle actually lands

## Slide 13: State Selection
L
L2
L3
Z2
Z
Planned Trajectory
Trajectory only for analysis

## Slide 14: State Selection
Every turn is on the basis of obstacle assessed at the next sweeping line while states are selected on the basis of the set hypotheses.

## Slide 15: Curve Generation
Connect L to L2 by a clothoid curve
Connect L2 to L3 by curve along the road length
Check feasibility
If infeasible, perform local optimization
If still infeasible, reduce speed/sweeping line step size and repeat

## Slide 16: Small Obstacle Problem
L
Z2 (original)
L3 (original)
L2 (original)
Z (original)
Z (modified)
Z2 (modified)
L3 (modified)
L2 (modified)
small obstacle
Z (original) cannot be used for obstacle analysis as it cannot detect the small obstacle and hence always return infeasibility. Hence it is modified to Z (modified) by reduction in step size of the sweeping line. Corresponding Z2s are Z2 (original) and Z2 (modified)

## Slide 17: Lane
Graph search gives the shortest path as output
Result consists of trajectory and all the expanded states
The expanded states together with available lateral bounds constitute a Lane
Trajectory may be modified by moving the expanded states laterally

## Slide 18: Graph generated

## Slide 19: Results

## Slide 20: Considering Multiple vehicles

## Slide 21: Problem
A number of vehicles with planned trajectories and lanes are given
Construct plan of the next vehicle entering the scenario
The trajectories of the other vehicles may be modified by changing their lanes (moving their expanded states laterally)

## Slide 22: Expansion Strategy
Expansion Strategy
Free State Expansion
Vehicle Following
Wait for Vehicle

## Slide 23: Free State Expansion
Expand using maximum speed, overtaking expansion strategy
Use sweeping line for obstacle analysis
Compute vehicles requiring independent lane
For every pathway
Distribute pathway width amongst the vehicles
Vehicle being followed or going ahead by a larger speed not considered
To skip details go to slide 32

## Slide 24: Strategy
Find vehicles (Rc) affected by altered navigation of Ra or Rb and hence also require a separate lane
Find vehicles (Rd) affected by altered navigation of Ra, Rb or Rc and hence also require separate lane
Find vehicles (Rb) affected by navigation of vehicle under planning (Ra) to Z and hence require a separate lane
And so on till no vehicle is further affected

## Slide 25: Region of independent lane
Region within which all vehicles have independent lanes
Region of independent lanes (S)
Vehicles requiring independent lanes (H)
Check if a vehicle in H while travelling in S affects any other vehicle Rj
Calculate region (S2) in which Rj assumes a new lane
Add S2
Add Rj

## Slide 26: Calculating new affected region
Let Ri be the vehicle being planned
Let Rj be the vehicle affected
Let Rk be any other vehicle which might be affected by Rj
Rj moves to new lane as soon as possible (a)
Rj returns to original planned lane after crossing navigation region of Ri (L to Z) , say (b)
New lane is effective in (a) to (b)
While Rj travels from (a) to (b), it should not affect any other vehicle (Rk). If yes, it is also added, and so on

## Slide 27: Calculating affected region
Ri
Ri
Rj
Rj
Rj
Ri
Rj
Rj
Ri
Rj
Motion from L to Z
(a)
(b)
(b)
(a)
Same side
Opposite sides

## Slide 28: Calculating affected region
While Rj travels from (a) to (b) , some Rk also travels as per its trajectory
Does Rj effect Rk, in which case the affected region and vehicles are updated and the process repeats?
Since motion of Rj from (a) to (b) is yet to be computed, approximations are used

## Slide 29: Calculating affected region
Rj
(a)
(b)
Rk
Rj
(a)
(b)
Rk
Same Side
If Rk is safe with Rj at (b), it is not affected, distances will only increase with Rk moving forward
Opposite Sides
If Rk moved by a threshold (proportional to speed) is safe with Rj at (b), it is not affected. With time Rk will get closer to Rj and may get affected. Maximum threshold assumed.

## Slide 30: Lane Distribution
Get vehicles requiring independent lane
Get preferred position for vehicle being planned
Check if placement possible without moving other vehicles
If not, check if placement possible with maintenance of maximum separation threshold
If not, compute total free space and distribute between vehicles evenly

## Slide 31: Free State Expansion
Z2
Z
(b)
(a)
Rj
Ri
Trajectory of Rj already covered
(this point and before)
Trajectory of Ri
Trajectory of Rj planned
Distribution of lanes amongst vehicles
Generated trajectories for vehicles
Computing lane vehicles
Original lane of Rj
Modified lane of Rj
Lane of Ri
Planned position of Rj
Planned position of Ri

## Slide 32: Vehicle Following
Select the vehicle to follow
Follow the selected vehicle
Laterally closest vehicle is selected
Speed is fixed to allow following with some distance
Z2 is taken as per reduced speed
Rest expansion same as free state expansion
Z is taken as per normal speed

## Slide 33: Vehicle Following
Trajectory of Rj already covered
(this point and before)
Trajectory of Ri
Trajectory of Rj planned
Z2
Z

## Slide 34: Wait for Vehicle
Consider a narrow bridge with a stream of vehicles coming from one side
Plan to wait for some of the vehicles in the stream to clear and hence go forward

## Slide 35: Wait for Vehicle
Decide the vehicle to wait for
Compute the position/ trajectory to wait
Modify other vehicle’s trajectories
Compute state after wait
Attempt for all vehicles in the crossing stream
Number of state expansions = number of vehicles in stream

## Slide 36: Computing the position of wait
Assume obstacle analysis line (Z) lies inside the narrow bridge
Assume previous line (Z2) lies outside the narrow bridge in a wide region
Maximum separation threshold is left
Two options to wait: Left of the leftmost vehicle in the stream, or Right from the rightmost vehicle in the stream
Whichever has minimum deviation from current position is selected

## Slide 37: Modification of Trajectories
Modify trajectory for the vehicle being waited for
Calculate time when it crosses the vehicle being planned
Modify trajectories of all other vehicles till this time
Get a snapshot of state after wait and use as the expanded state
Compute trajectory of the vehicle being planned
Calculate positions around waiting vehicle at Z2
Set the lateral position as constant in this region
Hence all overtaking and like behaviours get cancelled

## Slide 38: Wait for Vehicle Strategy
Z2
Z2
Z
Z2
Ri
Rk
Detection of sudden narrowing of width of road
Lane of Rk
Planned position of Ri
(a)
(b)
Modification of lane of Ri
Trajectory of Rk
Trajectory of Ri
The generated trajectory for vehicles

## Slide 39: Expansion strategy selection
All 3 strategies used for all state expansions results in too many expanded states
To limit expansions following heuristic rule is used
Strategy | Precondition
Free State Expansion | Parent state was expanded by free state expansion and no new vehicle encountered/left, a new vehicle encountered/left
Vehicle Following | Parent state was expanded by vehicle following and no new vehicle encountered/left, a new vehicle encountered/left
Wait for vehicle | Sudden change in road width used for obstacle assessment
Once decided to overtake/ follow a vehicle, continue doing so till a new vehicle approaches or leaves (changing overtake scenario)

## Slide 40: Results

## Slide 41: Results

## Slide 42: Results

## Slide 43: Results

## Slide 44: Analysis
Chart: Number of obstacles (n)
| 0 | 1 | 2 | 3 | 4 | 5 | 6
 | 0 | 1 | 4 | 11 | 22 | 52 | 131
Chart: Number of obstacles (n)
| 0 | 1 | 2 | 3 | 4 | 5 | 6
 | 37 | 72 | 158 | 214 | 300 | 709 | 1398

## Slide 45: Analysis
Chart: Number of vehicles in same direction (a)
| 0 | 1 | 2 | 3
 | 0 | 1 | 2 | 3
Chart: Number of vehicles in same direction (a)
| 0 | 1 | 2 | 3
 | 27 | 35 | 50 | 72

## Slide 46: Thank You
Acknowledgements:
Commonwealth Scholarship Commission in the United Kingdom
British Council