## Slide 1: Motion Planning for Multiple Autonomous Vehicles
Rahul Kala
Congestion Avoidance in City Traffic
Presentation of paper: R. Kala, K. Warwick (2015) Congestion Avoidance in City Traffic. Journal of Advanced Transportation, 49(4): 581–595.

## Slide 2: Key Contributions
Proposing city traffic as a scenario to study traffic congestion.
Proposing the importance of considering traffic lights in decision making regarding routes.
Proposing a simple routing algorithm that eliminates the high density of traffic and hence minimizes congestion.
Stressing frequent short term re-planning of the vehicle in place of long term (complete) infrequent re-planning.

## Slide 3: Assumption
Vehicles have very diverse speeds
Non-recurrent traffic (does not follow historical traffic patterns)
City traffic scenario
Objective
Minimize non-recurrent congestion

## Slide 4: City Traffic Scenario
S. No. | Characteristic | Highway Traffic | City Traffic
1. | Infrastructure | Less number of long length roads | Many short length roads (alternative roads) intercepting each other. Very computationally expensive routing.
2. | Vehicle Emergence | Distant entry/ exit points. New vehicles do not invalidate anticipated plans. | Many entry/ exit points at road ends/ between roads. Because of new vehicles, anticipation not possible.
3. | Planning Frequency | High anticipation favours long term planning | Low anticipation invalidates long term plans

## Slide 5: Routing Systems
Centralized Systems
Too computationally expensive
Decentralized Systems
Not considering other vehicles
Predicting using microsimulations
Systems forecasting based on historic data
Consider all possible motions
Causes high traffic congestion
Not valid for non-recurrent traffic
Computationally inefficient for too many vehicles/ re-plans
New vehicles invalidate plans/ require re-planning
All vehicles need to be intelligent
All vehicles need to be intelligent
Simulation uncertainties become large with time, diverse vehicles, overtakes, traffic signals
Routing
Limitations

## Slide 6: Planning Hypothesis
Make frequent effective short term plans
or, plan part of the route regularly as the vehicle moves
Frequent = Constantly adapt to changes
Short Term = Limit computational requirement

## Slide 7: Traffic Simulation
Driving Speed
  Intelligent Driver Model (standard model, converts vehicle separations into speed)
Lane Change
  Choose lane with maximize Time to Collision (if any in the current)
  Stay on the leftmost lane (if currently close to maximum speed)
  This allows other vehicles to overtake (from the right)

## Slide 8: Single Lane Overtake
Vehicles vary a lot in speeds and hence every overtake is important
Vehicle is allowed to move on the wrong side, overtake the slower vehicle and return to its lane
Vehicle are projected (with acceleration for the overtaking vehicle).
Overtake should be feasible as per projections with enough separations
Other vehicles may additionally cooperate post initiation of single lane overtake, to overcome uncertainties

## Slide 9: Single Lane Overtake
A
B
C
A
B
C
B
A
C
A
B
C
(a) A checks feasibility to overtake B while C is coming from opposite end
Arrows indicate separation checks. Since A and C are moving in opposite direction, needed separation is much larger.
(b) Projected positions of vehicles when A is expected to lie comfortably ahead of B
(c) Completion of overtake.

## Slide 10: Vehicle Routing
Hypothesis
Make frequent effective short term plans
(Re-)Plan at every crossing
Minimize
(i) Expected travel time
(ii) Expected traffic density
(iii) Expected time to wait at crossings
Plan for a threshold distance from the source
Assume it is possible to reach the goal from the planned state
Like human drivers always see the current traffic and take the best route towards the goal, assuming no dead ends

## Slide 11: Vehicle Routing
Let:
Arrows denote roads
Line Widths denote current traffic density
Heuristic costs to goal may replace actual costs after threshold
Source
Goal
Route 1: Long, Moderate density, more traffic lights
Route 2: Short, High traffic density, less traffic lights
Route 3: Preferable Long, Low traffic density, less traffic lights

## Slide 12: Vehicle Routing
maxHistorical
Selected Path
Current position
Current position
Selected Path
maxHistorical
Selected Path
Current position
Origin
Goal
(a) From current position the vehicle plans towards the goal and after maxHistorical cost stops the current search and moves by the best path
(b) After reaching the next crossing, change of plan takes place as per the new information available
(c) Vehicle finally reaches a point from where the goal is near

## Slide 13: Comparisons
S. No. | Method | Objective/ Frequency
1. | Optimistic (static) | Minimize expected travel time assuming highest speeds
2. | Pessimistic (static) | Minimize expected travel time assuming highest speeds, prefer roads with more lanes
3. | Traffic Messaging Channel (TMC, static) | Track vehicles to get immediate travel speeds (adapted for diverse speed vehicles), planned for only at the start
4. | TMC (dynamic) | S. No. 3, plan at every crossing
5. | Density (dynamic) | Minimize expected travel time by considering current traffic density, plan at every crossing
6. | TMC with traffic lights (dynamic) | S. No. 4, expected time waiting at the crossing added
7. | Density with traffic lights (dynamic) | Proposed method, S. No. 3, expected time waiting at the crossing added

## Slide 14: Results
Chart: Average Time of Completion of Journey
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45
optimistic | 16.0092 | 15.4501 | 16.5412 | 14.9276 | 16.4874 | 16.4031 | 18.1867 | 19.3249 | 18.7295
pressimistic | 15.7218 | 15.4798 | 16.6578 | 16.7711 | 18.6072 | 16.2826 | 18.3952 | 18.731 | 18.2495
TMC static | 15.4479 | 14.8794 | 15.601 | 15.6206 | 14.6218 | 15.2545 | 17.1123 | 16.5979 | 17.8736
TMC dynamic | 15.9166 | 15.1754 | 15.7306 | 16.3774 | 15.544 | 14.8291 | 18.2581 | 18.2198 | 18.1036
TMC with traffic lights | 10.1666 | 11.1569 | 13.5309 | 12.7306 | 14.1171 | 9.3482 | 12.5142 | 13.4744 | 14.9004
density | 15.1201 | 14.4816 | 14.6117 | 13.1044 | 13.734 | 13.6778 | 15.3011 | 15.4213 | 15.7233
density with traffic lights | 10.394 | 11.3471 | 11.5905 | 11.9897 | 13.5659 | 8.4927 | 9.7698 | 12.5802 | 13.2514

## Slide 15: Results
Chart: Average Distance Travelled
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45
optimistic | 3.9548 | 3.9878 | 3.9876 | 3.9999 | 3.9873 | 3.9754 | 3.9842 | 3.9847 | 3.9811
pressimistic | 3.9471 | 3.9811 | 3.987 | 3.9942 | 3.9834 | 3.974 | 3.9788 | 3.9798 | 3.9703
TMC static | 3.8413 | 3.7057 | 3.6287 | 3.5191 | 3.3703 | 3.3882 | 3.3444 | 3.2444 | 3.166
TMC dynamic | 3.9273 | 3.8554 | 3.8746 | 3.8237 | 3.8075 | 3.7855 | 3.709 | 3.7454 | 3.7191
TMC with traffic lights | 2.9198 | 2.8415 | 2.9368 | 2.87 | 2.9295 | 2.6225 | 2.8187 | 2.8935 | 2.9193
density | 3.7453 | 3.7052 | 3.5567 | 3.5237 | 3.4269 | 3.3546 | 3.292 | 3.1976 | 3.1273
density with traffic lights | 3.0172 | 2.9626 | 2.8864 | 2.8277 | 2.7906 | 2.4254 | 2.4806 | 2.5751 | 2.5327

## Slide 16: Results
Chart: Average Speed
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45
optimistic | 14.8221 | 15.4866 | 14.4641 | 16.077 | 14.5103 | 14.5413 | 13.1444 | 12.3717 | 12.9965
pressimistic | 15.0637 | 15.4307 | 14.3609 | 14.2895 | 12.8447 | 14.6439 | 12.9776 | 12.7482 | 13.0534
TMC static | 14.9198 | 14.9431 | 13.9556 | 13.5171 | 13.8299 | 13.3268 | 11.7264 | 11.7284 | 10.6279
TMC dynamic | 14.8046 | 15.2433 | 14.7784 | 14.0086 | 14.697 | 15.3165 | 12.1884 | 12.3342 | 12.3262
TMC with traffic lights | 17.2318 | 15.2809 | 13.0227 | 13.5265 | 12.451 | 16.8323 | 13.5145 | 12.8843 | 11.7553
density | 14.8623 | 15.3512 | 14.6049 | 16.1339 | 14.9713 | 14.7156 | 12.9087 | 12.4408 | 11.9337
density with traffic lights | 17.417 | 15.6656 | 14.9419 | 14.1504 | 12.3422 | 17.1352 | 15.234 | 12.2816 | 11.4677

## Slide 17: Results
Chart: Average Time of Completion of Journey
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45
with overtaking | 11.783 | 12.2981 | 11.6648 | 11.642 | 10.2719 | 11.1066 | 12.033 | 12.354 | 10.8513
without overtaking | 20.9544 | 20.2511 | 20.7536 | 22.2772 | 21.8772 | 20.7697 | 21.0325 | 20.9727 | 22.1663
Results with and without single lane overtaking

## Slide 18: Thank You
Acknowledgements:
Commonwealth Scholarship Commission in the United Kingdom
British Council