## Slide 1: Motion Planning for Multiple Autonomous Vehicles
Rahul Kala
Conclusions

## Slide 2: Conclusions
Thesis
Trajectory Generation
Intelligent Management of the Transportation System

## Slide 3: Trajectory Planning Considering a single vehicle
S. No. | Algorithm | Optimality | Completeness | Computation Time, Scalability, Iterative (if deliberative)
1. | Genetic Algorithm | Optimal. More exploitative version was implemented, which meant less global optimality. | Probabilistically Complete for a reasonable number of obstacles | Little High, Reasonably scalable, Yes
2. | Rapidly-Exploring Random Trees (RRT) | No | Near-Complete | Fair, Largely scalable, No
3. | RRT-Connect | Locally optimal, Globally optimal for simple cases | Near-Complete | Fair, Largely scalable, No
4. | Multi Level Planning | Generally optimal. Can miss overtakes with very fine turns | Near-Complete | Little high, Poorly scalable, No
5. | Planning using dynamic distributed lanes | Generally optimal. Can miss overtakes with very fine turns | Near-Complete | Somewhat high, Poorly scalable, No
6. | Fuzzy Logic | No | No | Very Low, Completely Scalable, N/A
7. | Lateral Potentials | No | No | Very Low, Completely Scalable, N/A
8. | Elastic Strip | Generally optimal. Can miss very fine turns | Near-Complete (less than 2, 3, 4 and 5) | Medium, Very scalable (more than 2 and 3), N/A
9. | Logic based planning | Locally near-optimal. (less than 3) | No (more than 6 and 7) | Low, Almost completely scalable, N/A

## Slide 4: Trajectory Planning Considering a single vehicle
Optimality (more to less): Planning using Dynamic Distributed Lanes, Multi Level Planning, GA, RRT-Connect, RRT, Elastic Strip, Logic Based Planning, Lateral Potentials, and Fuzzy Logic.
Completeness (more to less): GA, RRT-Connect/RRT, Multi Level Planning, Planning using Dynamic Distributed Lanes, Elastic Strip, Logic Based Planning, Lateral Potentials and Fuzzy Logic.
Computational time (least to highest): Fuzzy Logic, Lateral Potentials, Logic Based Planning, Elastic Strip, Multi Level Planning, Planning using Dynamic Distributed Lanes, RRT-Connect, RRT and GA.

## Slide 5: Trajectory Planning Coordination
S. No. | Algorithm | Coordination | Communication, Assumptions | Optimality | Computational complexity
1. | Genetic Algorithm | Traffic inspired heuristics for path/speed, Prioritization | Yes, Vehicles stay on their left sides mostly | Sub-optimal, Global knowledge makes it more desirable | Somewhat high to continuously alter speed and check overtake feasibility. Computation is distributed as the vehicle travels
2. | Rapidly-Exploring Random Trees (RRT) | Prioritization, Attempt to maintain maximum collision-free speed | Yes, One way traffic only | Non-cooperative, Sub-optimal | A little high due to multiple attempts to compute speed
3. | RRT-Connect | Prioritization, Vehicle following/ overtake based speed determination | Yes, One way traffic only | Non-cooperative, Sub-optimal | Small time needed to decide between overtaking and vehicle following
4. | Multi Level Planning | Layered Prioritization, Each layer uses separation maximization heuristic, Vehicle following/ overtaking based speed determination | Yes | Largely optimal | High due to a large number of re-planning of different vehicles at different levels
5. | Planning using dynamic distributed lanes | Pseudo-centralized, Each state expansion uses separation maximization heuristic, Vehicle following/ overtaking based speed determination | Yes | Largely optimal, Cooperation can be slow | High as part trajectories of a number of vehicles need to be continuously be altered

## Slide 6: Trajectory Planning Coordination
S. No. | Algorithm | Coordination | Communication, Assumptions | Optimality | Computational complexity
6. | Fuzzy Logic | Vehicles treated as obstacles, Distances assessed for overtaking decision making, Speed controlled by fuzzy rules | No, Vehicles stay on their left sides mostly, Roads not too wide to accommodate multiple vehicles per side of travel | Sub-optimal, Not accounting for global knowledge makes it undesirable | Nil
7. | Lateral Potentials | Vehicles treated as obstacles, Always overtake strategy, Distance from front used for deciding speed | No, One way only | Sub-optimal, Not accounting for global knowledge makes it undesirable | Nil
8. | Elastic Strip | Vehicles treated as moving obstacles, Always overtake strategy, Distance from front used for deciding speed | No, One way only | Sub-optimal, Not accounting for global knowledge makes it undesirable | Very small time needed to extrapolate vehicle motion
9. | Logic based planning | Vehicles treated as moving obstacles, Lateral distances measured for overtake decision making, Distance from front used for deciding speed | No, Vehicles stay on their left sides mostly | Sub-optimal, Cooperation can be slow, Not accounting for global knowledge makes it undesirable | Very small time needed to extrapolate vehicle motion

## Slide 7: Trajectory Planning Coordination
Coordination
Computational Expense
Cooperation
Deliberative
Reactive
Cooperative
Non-cooperative
Overtaking
Always overtake
Compute feasibility
Speed Determination
Immediate best
Optimized assignment

## Slide 8: Intelligent Transportation Systems
S. No. | Concept | Features
1. | Routing objective/ considerations | traffic density, congestion control, risk, traffic lights, expected travel time, best/worst travel time, time to reach destination, start time, booked road (travel cost)
2. | Routing frequency | frequent re-planning, fixed plans, incomplete or complete plans
3. | Routing traffic assumptions | recurrent, non-recurrent, recurrent with some possibility of non-recurrent trends
4. | Traffic Lights | cyclic, earliest vehicle first based, most late vehicles first based
5. | Lane change | overtake based (extra lane primarily used for overtaking), cooperative to vehicles running more late, dynamic speed limit based, booked lane (travel cost)
6. | Traffic | entirely semi-autonomous, mixed, manual

## Slide 9: Thank You
Acknowledgements:
Commonwealth Scholarship Commission in the United Kingdom
British Council